## Slide 1: IMWEBs Online Database Design (animation)
Project tables
Support tables
User tables
GIS layers
subfield
id INT (PK) watershed_id INT subfield INT area REAL
reach
id INT (PK) watershed_id INT reach INT length REAL receive_reach_id INT
field
id INT (PK) watershed_id INT field INT area REAL
outlet
id INT (PK) watershed_id INT point INT
watershed
id INT (PK) name VARCHAR(255) alias VARCHAR(20) description TEXT area REAL last_update TIMESTAMP
watershed_bmp
id INT (PK) watershed_id INT bmp_id INT
bmp_combo
id INT (PK) bmp_id INT last_update TIMESTAMP
bmp
id INT (PK) name VARCHAR(255) description TEXT bmp_group_id INT selection_type_id INT last_update TIMESTAMP
bmp_cost_benefit
id INT (PK) ScenarioId INT year INT net_return_change REAL runoff_change REAL sediment_change REAL dp_change REAL pp_change REAL dn_change REAL pn_change REAL carbon_change REAL biodiversity_change REAL net_return_change REAL runoff_onsite_change REAL sediment_onsite_change REAL dp_onsite_change REAL pp_onsite_change REAL dn_onsite_change REAL pn_onsite_change REAL carbon_onsite_change REAL biodiversity_onsite_change REAL last_update TIMESTAMP
watershed_user
watershed_id INT user_id INT
user
id INT (PK) first_name VARCHAR(45) last_name VARCHAR(45) email VARCHAR(50) password VARCHAR(48) user_role_id INT address_id INT active BOOLEAN last_update TIMESTAMP
watershed_bmp_location
id INT (PK) watershed_bmp_id INT location_id INT
Notes:
PK means primary key
means one to many relationship
user_role
id INT (PK) type VARCHAR(20) description TEXT last_update TIMESTAMP
How optimization works:
All BMP (including combination) benefits and cost are saved in subfield scale
Lookup tables will be used to convert user selected BMP locations (e.g., list of field or stream IDs) to subfield IDs.
Then we can know in each subfield what BMP has been selected, which gives the bmp_combo_id
Now, we can get BMP cost and benefits at each subfield. These information will be input to optimization model
With constraint (e.g. TP reduction of 15% to 20%) and optimize mode (e.g., maximize benefits, or minimize cost), optimization model will give a recommended BMP combo type (1 or more BMP) for each subfield.
Then we can use the lookup table to convert BMP subfield list back to BMP selection location IDs for interface display.
baseline_subfield
subfield_id INT (PK) year INT water REAL sediment REAL pp REAL dp REAL pn REAL dn REAL biodiversity REAL carbon REAL yield REAL revenue REAL cost REAL net_return REAL last_update TIMESTAMP
baseline_reach
reach_id INT (PK) year INT water REAL sediment REAL pp REAL dp REAL pn REAL dn REAL last_update TIMESTAMP
selection_type
id INT (PK) type VARCHAR(20) gis_layer VARCHAR(20) last_update TIMESTAMP
bmp_group
id INT (PK) type VARCHAR(20) description TEXT last_update TIMESTAMP
address
id INT (PK) address VARCHAR(50) address2 VARCHAR(50) city_id VARCHAR(50) postal_code VARCHAR(10) user_role_id INT phone VARCHAR(20) last_update TIMESTAMP
city
id INT (PK) city VARCHAR(50) country_id INT last_update TIMESTAMP
country
id INT (PK) country VARCHAR(50) last_update TIMESTAMP
project
id INT (PK) name VARCHAR(255) description TEXT user_id INT watershed_id INT status_id INT opt_mode_id INT start_year INT end_year INT is_increment_mode BOOLEAN iteration_num INT is_optimization_run BOOLEAN create_time TIMESTAMP last_update TIMESTAMP
constraint
id INT (PK) type VARCHAR(50) last_update TIMESTAMP
optimizatioin_mode
id INT (PK) mode VARCHAR(20) last_update TIMESTAMP
project_constraint
project_id INT constraint_id INT upper REAL lower REAL
project_bmp
id INT(PK) project_id INT bmp_id INT
project_bmp_location
project_bmp_id INT location_id INT
status
id INT (PK) type VARCHAR(20) last_update TIMESTAMP
optimization_result_iteration
id INT (PK) project_id INT net_return_change (bmp cost) REAL runoff_change REAL sediment_change REAL dp_change REAL pp_change REAL dn_change REAL pn_change REAL carbon_change REAL biodiversity_change REAL runoff_change_frac REAL sediment_change_frac REAL dp_change_frac REAL pp_change_frac REAL dn_change_frac REAL pn_change_frac REAL carbon_frac_change REAL biodiversity_change_frac REAL
optimization_result_iteration_bmp
id INT (PK) optimization_result_iteration_id INT selection_type_id INT location_id INT bmp_combo_id INT net_return_change (bmp cost) REAL runoff_change REAL sediment_change REAL dp_change REAL pp_change REAL dn_change REAL pn_change REAL carbon_change REAL biodiversity_change REAL
watershed_boundary
id INT (PK) watershed_id INT area REAL
user_field
id INT(PK) user_id INT field_id INT
user_field_bmp
user_field_id INT(PK) bmp_id INT rating INT
How what-if BMP analysis works:
All BMP (including combination) benefits and cost are saved in subfield scale
Lookup tables will be used to convert producer field(s) to subfield IDs
From bmp_cost_benefit table we can get selected BMP benefits and costs in these subfields
Then we can use the lookup table to convert BMP benefits and costs back to producer field(s) scale for interface display.
Small dam,
Reservoir
Catch basin
Wetland
Feedlot
Manure Storage
Pond
Dugout
Field
Reach
Outlet
Boundary
Farm